## Slide 1: Prosthetic Hand Control via Shoulder Movement
Nitay ozer
Itay mal
supervisor KobY Kohay

## Slide 2: Problem Definition
Wirelessly controlling Haifa 3D robotic prosthetic hand
  Using user’s shoulder movements

## Slide 3: Existing solution- Mechanical Straps
Pros:
  Simple
  Reliable
  Independent of power source
Cons:
  Requires a lot of physical effort to operate
  Limited in DOF
  Unnatural look

## Slide 4: Existing solution- Myoelectric (EMG) Control
Pros:
  High variety of DOF
  Can look like natural arm
  Intuitive operation*
Cons:
  Expensive
  Heavy
  High power consumption
  Phantom pain*

## Slide 5: Previous Work- Shunit Polinsky
Reach to Grasp
  IMU based method
  Recognition of natural movement patterns

## Slide 6: Possible Approaches

## Slide 7: Mode Cycling
Pros:
  Easier movement identification
  Less actions to remember
Cons:
  Less immediate operation
  Need to remember state sequence
Next Mode
On/Off
Prev. Mode

## Slide 8: Mode Mapping
M1
M2
M3
M4
M5
Idle
Pros:
  Immediate activation of wanted mode
Cons:
  Harder movement identification
  Need to remember state location
  Limited amount of accessible modes

## Slide 9: Complex Gestures Mode Mapping
M1
M2
M3
Pros:
  Immediate activation of wanted mode
  More modes accessible
Cons:
  Even harder movement identification
  More complex gestures to learn
  May look awkward

## Slide 10: Classification Algorithms

## Slide 11: LSTM
Pros:
  Adequate to temporal data
  May be used as classifier
Cons:
  Computationally expensive
  Hard to implement for microcontroller
  Many learned parameters

## Slide 12: GRU
Pros:
  Adequate to temporal data
  May be used as classifier
  Slightly less parameters than LSTM
Cons:
  Computationally expensive
  Hard to implement for microcontroller
  Many learned parameters
  Less weight for long term memory

## Slide 13: Random Forest
Pros:
  Easy and fast training
  Highly fitted to classification tasks
  Explainable
  Fitted to microcontroller easily
Cons:
  Not designed for temporal data

## Slide 14: Purposed Solution

## Slide 15: Block Diagram
Our System
IMU Sensors
ESP32
Shoulder Movement

## Slide 16: Simplified Mode Cycling
Next Mode
On/Off

## Slide 17: Forward / Back Symmetry

## Slide 18: Program Flow
Sample rate – 80Hz
Buffer size – 100 timepoints
Prediction after each sample
Capture window prevents multiple hits from single gesture
BLE disconnection interrupts flow

## Slide 19: System Interconnection
ESP 32
IMU
Buzzer
3.7V Battery

## Slide 20: Development Process

## Slide 21: Data Acquisition
ESP connected to computer to collect sample traces to CSV files
Traces include target gestures as well as miscellaneous activities

## Slide 22: Data Labeling
Data traces trimmed and labelled using GUI

## Slide 23: Classifier Training
Random Forest classifier was trained using Scikit-Learn python package.
Chosen architecture:
  20 estimators
  Max depth 5
  Returns #Votes per class

## Slide 24: Real Time Program
Used common libraries to read sensors
ML model converted to CPP using utility script
Prediction decision is done by thresholding 70% of votes

## Slide 25: Demo

## Slide 26: Further Work Suggestions
Improve classification accuracy
Battery life testing and optimization
Detect more gestures
Improve physical product
User feedback